## Slide 1
Mobile Intelligent Robotic Arm Interface (MIRAI)
Progressive Development of an Autonomous Omnidirectional Robotic Arm
Team: Livity Labs
Mentor: Dr. Kishore Ayyala Ajay Kumar—K.R. Mangalam University, School of Engineering & Technology

## Slide 2
Problem Statement & Goal
The Problem
Most low-cost robotic arms are either fully manual or attempt full autonomy in one leap — making them hard to validate, debug, and defend as a working system. There is no gradual, testable pathway from a simple manipulator to an autonomous mobile robot that a student team can realistically build stage by stage.
Our Goal
Develop a 6-DOF robotic arm mounted on an omnidirectional mobile platform that evolves across three clearly defined stages — from a manually controlled manipulator into a fully autonomous pick-and-place robot.
Current focus: Stage 1 — proving the arm can physically perform accurate manipulation before adding mobility or autonomy.

## Slide 3
Project Development Pipeline
Three progressive stages — each validates one capability before the next is added. This staged approach ensures every subsystem is proven and debuggable before complexity increases.
Fixed Robotic Arm
Mobile Omnidirectional Arm
Autonomous Mobile Manipulator
Each stage builds on the last, creating a verifiable, incremental path from a basic manipulator to a fully autonomous mobile robot.

## Slide 4
Stage 1 — Fixed Robotic Arm
Objective
Build and validate the 6-DOF robotic arm as a stationary manipulator before introducing mobility or autonomy.
Main Task
Successfully pick a LEGO or small object using the camera for detection, and place it at a new location — using fully manual control.
Testing Focus
Test all 6 DOF & servo movement, arm positioning accuracy, gripper opening/closing, object picking & placement, and validate mechanical design.

## Slide 5
Stage 1 — Pick & Place Pipeline
Before making the robot autonomous, we must prove the arm itself can physically perform accurate manipulation. This 8-step sequence validates the full manual control loop.
01
Object Detected / Observed
02
User Controls Arm
03
Arm Moves to Object
04
Gripper Closes
05
Object Picked
06
Arm Moves to Destination
07
Gripper Opens
08
Object Placed Successfully

## Slide 6
Components List — Stage 1
Category | Component Name | Qty | Unit Price | Total Cost
Actuators | MG996R 180° Servos (9.4 kgf·cm) | 3 | ₹1,317/pack | ₹1,317
Actuators | MG90S Metal-Gear Servos (2.2 kg·cm) | 3 | ₹439 | ₹439
Control | PCA9685 16-Channel Servo Driver | 1 | ₹480 | ₹480
Main Brain | ESP32 Dev Board + GPIO Expansion | 1 ea | ₹342 / ₹219 | ₹561
Vision | ESP32-CAM (OV2640) | 1 | ₹849 | ₹849
Power | 3S LiPo Battery 2200mAh + iMAX B6 Charger | 1 ea | ₹1,899 / ₹2,689 | ₹4,588
Power | XL4015 5A Buck Converter | 1 | ₹249 | ₹249
Wiring | Jumper Wires, Extension Cables, Shrink Wrap | — | — | ₹698

## Slide 7
System Assembly — Mechanical Layout

## Slide 8
Components Used — Control & Vision
ESP32 Development Board
Main controller — handles servo PWM generation, camera interface, and serial communication.
ESP32-CAM (OV2640)
Vision input for object detection and live feed. Streams video for manual guidance.
GPIO Expansion Board
Breaks out ESP32 pins for easier wiring to servos, sensors, and peripherals.
MG996R Servo Motor
High-torque servos (9.4 kgf·cm) for the base, shoulder, and elbow joints.
SG90 Micro Servo
Lightweight servos for wrist rotation and gripper actuation.
PCA9685 Servo Driver
16-channel I²C PWM driver — controls all 6 servos from the ESP32 with a single wire pair.

## Slide 9
Components Used — Power & Accessories
3S LiPo Battery (2200mAh)
11.1V main power source — delivers high current for all six servos simultaneously.
iMAX B6 Balance Charger
Safely charges and balances the LiPo pack, protecting battery health and longevity.
XL4015 Buck Converter
Steps down battery voltage to a stable 5V rail for the ESP32 and servo driver.
FTDI Programmer (USB-TTL)
Flashes firmware to the ESP32 and provides serial debug output during development.
ESP32-CAM Extension Board
Provides accessible GPIO pins and a USB interface for the ESP32-CAM module.
Servo Extension Cables
30 cm extensions route signals cleanly from the driver to each servo joint.

## Slide 10
The Future of Care: Our Motivation
The MIRAI project transcends pure engineering; it's driven by a vision to create accessible, assistive technology with genuine human impact.
We envision a future where autonomous robotic arms can support elderly individuals living alone. From fetching daily medications to providing immediate alerts to family in case of an unforeseen event or malfunction, MIRAI aims to enhance safety, independence, and peace of mind for both seniors and their loved ones. This project is about empowering lives through practical, compassionate innovation.