## Slide 1
LIPO battery 22mah 3s
ESP32 Development Board
XL4015 5A Buck Converter
PCA9685 16-Channel Servo Driver
Schematics
From Source | Pin / Terminal | To Destination | Pin / Terminal | Purpose
3S LiPo Battery | Red Wire (+) | XL4015 Buck Converter | IN+ | Raw 11.1V Battery Input
3S LiPo Battery | Black Wire (-) | XL4015 Buck Converter | IN- | Battery Ground
XL4015 Output | OUT+ (Set to 6.0V) | PCA9685 Driver | Green Screw Terminal V+ | Servo Power Rail
XL4015 Output | OUT- (GND) | PCA9685 Driver | Green Screw Terminal GND | Motor Ground
XL4015 Output | OUT+ (Set to 6.0V) | ESP32 Expansion Board | VIN (or 5V) | Board Main Power
XL4015 Output | OUT- (GND) | ESP32 Expansion Board | GND | Shared System Ground
From Source (ESP32 Expansion Board) | Pin / Terminal | To Destination (PCA9685 Driver) | Pin / Terminal | Purpose
ESP32 Expansion Board | 3.3V | PCA9685 Driver | VCC | Logic Power for Driver IC
ESP32 Expansion Board | GND | PCA9685 Driver | GND | Shared Signal Ground
ESP32 Expansion Board | GPIO 21 | PCA9685 Driver | SDA | I2C Data Line
ESP32 Expansion Board | GPIO 22 | PCA9685 Driver | SCL | I2C Clock Line

## Slide 2
MG996R Metal Gear Servo Motor
MG996R Metal Gear Servo Motor
MG996R Metal Gear Servo Motor
MG90S Metal Gear Micro Servo Motor
MG90S Metal Gear Micro Servo Motor
MG90S Metal Gear Micro Servo Motor
PCA9685 Channel | Wire Alignment | Connected Servo | Joint Control
Channel 0 | Yellow/Orange (PWM), Red (V+), Brown/Black (GND) | MG996R | Base Rotation
Channel 1 | Yellow/Orange (PWM), Red (V+), Brown/Black (GND) | MG996R | Shoulder Lift
Channel 2 | Yellow/Orange (PWM), Red (V+), Brown/Black (GND) | MG996R | Elbow Movement
Channel 3 | Yellow/Orange (PWM), Red (V+), Brown/Black (GND) | MG90S | Wrist Pitch
Channel 4 | Yellow/Orange (PWM), Red (V+), Brown/Black (GND) | MG90S | Gripper Actuation
Channel 5 | Yellow/Orange (PWM), Red (V+), Brown/Black (GND) | MG90S | Camera Mount / Spare Joint